## Slide 1: Data Transfer Schemes

## Slide 2: Data Transfer Schemes
Data is transferred between
  Microprocessor and memory
  Microprocessor and I/O
  Memory and I/O

## Slide 3: Classification
Parallel and Serial
  Parallel classified as:
    Programmed I/O
        Synchronous
        Asynchronous
        Interrupt driven
    Direct Memory Access
        Burst mode
        Cycle stealing mode
  Serial classified as:
    Using hardware
    Using software

## Slide 4: Programmed Data Transfer
Used when relatively small amount of data is to be transferred between slow devices
Can be classified as
  Synchronous Transfer
  Asynchronous Transfer
  Interrupt driven data transfer

## Slide 5: Synchronous Data Transfer
Simplest
Used when the speed of the device is almost compatible with that of the processor
Whenever data is needed suitable instruction is issued
By the end of the execution of the instruction the transfer would be completed
Used when the timing characteristics of the device is known

## Slide 7: Asynchronous Data Transfer
Used when the speed of microprocessor and I/O devices do not match
Microprocessor initiates the data transfer by requesting the device to get ready
Then it goes on checking the status
When the device is ready it sends an acknowledgement
Handshaking
A lot of CPU time wasted in the loop checking the status

## Slide 8
Start
Send get ready signal to the I/O device
Is the Device ready?
Execute I/O instructions
Stop
Yes
No

## Slide 9: Interrupt Driven Data Transfer
The processor initiates the data transfer by requesting the device to get ready
It then goes on executing its original program
When the device is ready it sends an interrupt signal to the processor
Processor completes the current instruction, saves the status in the stack and branches to the ISS

## Slide 11: DMA Data Transfer
Burst Mode
Cycle Stealing

## Slide 13
Serial
  Using software: RIM ,SIM instructions
Hardware
  Using USART 8251